## Slide 1: Development of an SRAD Flight Computer
UB Students for the Exploration and Development of Space

## Slide 2: Flight Computer Requirements
Track and record flight telemetry
Deploy recovery system
Reliable GPS tracking
Record video (Optional)

## Slide 3: Component Selection
Teensy 3.5: Speed, space, SD card, Arduino compatibility
BMP280: Fast, easy to use
ADXL345: Fast, easy to use
MTK3339: Easy to use, ext. ant. capability
XBee-PRO 900HP: Proven component

## Slide 4: PCB Design
Reusable modules
Separate ignition battery

## Slide 5: Tracking
GPS for precise positioning, simple RDF backup for bad signal conditions
Custom RDF transmitter with 40 hour battery life
Redundancy:
  Primary flight computer with GPS tracking
  COTS GPS tracker
  Main section SRAD RDF tracker
  Tail section SRAD RDF tracker

## Slide 6: Kalman Filter For Apogee Detection
Combines Senor measurements with theoretical system dynamics
Pros
  Improved state estimation
  Sensor fusion
Cons
  Added complexity
  Kalman filters are linear, rocket dynamics are inherently nonlinear.
https://en.wikipedia.org/wiki/Kalman_filter

## Slide 7: Kalman Filter (Part 2)
Simplified Rocket Dynamics
   This is nonlinear
  ,
  This means that near apogee the rocket dynamics are linear

## Slide 8: Testing
Attached to custom built high-thrust quadcopter for quasi-ballistic launch simulation.
Test 1
  Late apogee detection observed.
  Kalman filter calibration corrected.
Test 2
  Unreliable operation.
  Faulty accelerometer replaced.
Test 3
  Accurate and reliable apogee detection observed.

## Slide 9: Conclusion
Future design
  Optimization
    Price, size, power usage, battery requirement, etc.
  SRAD radio
Working flight computer
  Kalman filter apogee detection
  Data logging
  Live telemetry
  GPS and RDF tracking